## Slide 1: Inverse kinematics
Pseudo inverse and redundancy
Chapter 3.

## Slide 2: Direct and inverse functions
Direct geometry
  h: q  h(q), C1 continuous function
Direct kinematics
  v: q,  v (q,) = J(q)
Inverse geometry
  Ill defined, singular points
  Numerical inversion by Newton descent
Integration of the descent
  Robot trajectory
  Quadratic problem at each step
v1
v2

## Slide 3: A linear minimization solution
Ax = b
If A is not invertible, two cases:
  There is no way to reach b
  x* = argmin ||Ax-b||
  = { x, so that ||Ax-b|| = min ||Ax-b|| }
  There is many optimal solutions for x
  x* = min { x so that x = argmin ||Ax-b|| }
x* = min argmin ||Ax-b|| .
= A+ b

## Slide 4: Pseudo inverse definition
The four conditions of Moore & Penrose
  A A+ A = A
  A+ A A+ = A+
  A A+ is symmetrical
  A+ A is symmetrical

## Slide 5: Pseudo inverse definition
  A A+ A = A
  A+ A A+ = A+
  A A+ is symmetrical
  A+ A is symmetrical
A A+ A x = A x
b*: reachable point
Projector
into A range
Solution for b*

## Slide 6: Pseudo inverse definition
  A A+ A = A
  A+ A A+ = A+
  A A+ is symmetrical
  A+ A is symmetrical
A+ A A+ b = A+ b
Projector
into A kernel
Solution for b
“twin” for b

## Slide 7: A linear minimization solution
Ax=b
x* = min argmin ||Ax-b||= A+ b
Specific cases
If A is invertible
  argmin ||Ax-b||=0
  unique solution to reach the minimum
A
x
b
=

## Slide 8: A linear minimization solution
Ax=b
x* = min argmin ||Ax-b||= A+ b
Specific cases
Few lines, many columns
  It is not possible to reach ||Ax-b||=0
  Unique solution to reach the minimum
A
x
b
=
x=a
x=b
x
a
b
x*
A+ = (AT A)-1 AT
Notes: Ax-b = A(x-z) + (Az –b) with z=Ap b // both being orthogonal since A’ A Ap b – b = 0

## Slide 9: A linear minimization solution
Ax=b
x* = min argmin ||Ax-b||= A+ b
Specific cases
Few lines, many columns
  argmin ||Ax-b||=0
  Many solutions to reach the minimum
A
x
b
=
x1
x2
x1=a
a
argmin
A+ = AT (A AT)-1
Notes: Si Ax=b, A x = Ap b + x - Ap A x = Ap b + N x, both being orthogonal

## Slide 10: Computing the pseudo inverse
Singular Value Decomposition (SVD)
Proof using the 4 Moore-Penrose conditions
  (with UUT=I and VVT=I)
Might be seen as a constructive definition
A
U
VT
1
m
=
…
0
0
0
0
A+
UT
V
1+
m+
=
…
0
0
0
0

## Slide 11: What is a task?
Sensor
4
1
2
3
4
1
2
3
Robot position: Robot control input:
An error between current and desired sensor values
A reference behavior of the error
The associated Jacobian matrix
Classical control law
[Samson91],[Espiau91]
Sensor
-
+

## Slide 12: Control in the task space
Configuration space VS task space
Easy motion specification
Reusability - versatility
Deformation of the motion
Sensor feedback
position
position 6d
gaze
center of
mass
parallelism
joint
limits
relative
pose

## Slide 13: Task redundancy
z can be used to vary the trajectory (obstacle avoidance)
P
?
We will use z to realize at best the second elementary task
[Rosen60],[Liegeois77]